Bo’ness Children’s Fair Festival

Traffic Management

Scope of Works

- This document details the operations for the implementation, maintenance and removal of Traffic Management prior to, during and after the Bo’ness Childrens Fair Festival.

Definitions

N/a

Location

The location of the work is within the confines of Bo’ness between Grahamsdyke Road, Linlithgow Road, Main Street and Grange Loan (and other connecting side streets)

Safety Issues

Personal Protective Equipment (PPE)

- Hard Hat/Bump Caps BS EN 397

- Eye Protection BS EN 116

- High Visibility Long Sleeve Jacket or Vest Class 3 BS EN 471

- High Visibility Yellow Trousers Class 3 BS EN471

- Steel Capped Safety Boots EN ISO 20347

- Gloves BS EN 388

Communications

- Motorola Two Way Band Radios

Method of Carrying out the works

Planning prior to setting up T.M.

- Locations assessed for the proposed works to ensure it is safe and practicable to carry out the works:-

- Length and Duration of Fair Parade

- Local Access and Emergency Vehicles

- Weather fog, rain, etc. other events

- Pedestrians

- Safety Zones

- Proximity of junctions at Main Junctions and Pinch Points for access to Bo’ness

- Manual Handling of Work Force and Implementation during Timescales

T.M. Equipment

- Crowd Control Barrier (areas that require access for parade)

- 1m Traffic Management Big Foot Cones (side streets within the cordoned off area)

- Rhino RB1 1000 Link Barriers (for Pinch Point Locations)

- Safety Rope (used at Cadzow Crescent and Dean Road Junction)

- Diversionary Signs (as per drawing 17-Bo’ness-ch-Fr-fest-002-Final)

Advance Sign of Event Day

- Advance Signage will be erected at the end of each main route to state “Restricted Access to XXXX between 08:00 and 16:00 on 30th June 2017 Bo’ness Childrens Fair. Up by WC 12th June 2017

- Signage will be placed at following Locations

  - Grahams Dyke/Harbour Road Junction

  - Linlithgow Rd and Deans Rd Junction

  - Seaview Place Roundabout heading towards Main Street

  - Bridgeness Rd/Cowdenhill Junction

  - Grangemouth Rd at Junction with Kinniel Rd

Setting out T.M. (Pre-event)

- On the day before the event, to minimise excessive disruption on the event morning and to decrease manual handling expectations for set out, Diversionary Signs, Cones and Barriers will be pre-set at the following times:

  - 29/06/17 – 10:00-15:00 Diversionary Signs and Steel/Rhino Barriers

  - 29/06/17 – 19:00-22:30 Barriers and Cones preset in their designated areas in accordance to drawing 17-Bo’ness-ch-Fr-fest-002-Final

T.M. Implementation (Event Day)

- Traffic Management Operatives will commence implementing side Street Closures along the Grahamsdyke Road, starting at Gauze Street and Kinglass, ,moving progressively Westward in a circular movement through the town on the Timings in Table 1 below (and stated in Letters Distributed by Organising Committee to residents):

Table 1

| Approx On Time | Location | Equipment |
| --- | --- | --- |
| 08:00-09:00 | Grahamsdyke Terrace/Grahamsdyke Rd | Cones/Road Closed |
| 08:00-09:00 | Grahamsdyke Lane/Grahamsdyke Rd | Cones/Road Closed |
| 08:00-09:00 | Craigallan Park/Grahamsdyke Rd | Cones/Road Closed |
| 08:00-09:00 | Grahamsdyke Ave/Grahamsdyke Rd | Cones/Road Closed |
| 08:00-09:00 | Gauze Rd/Grahamsdyke Rd | Rhino RB1/Road Closed |
| 08:00-09:00 | Kinglass Ave/Grahamsdyke Rd | Rhino RB1/Road Closed |
| 08:00-09:00 | Dean Rd/Erngath Rd | Steel Barrier/Road Closed |
| 08:00-09:00 | Dean Rd/Dugald Stewart Ave | Cones/Road Closed |
| 08:00-09:00 | Dean Rd/Marchlands Ave | Cones/Road Closed |
| 08:00-09:00 | Cadzow Cres and Ave/Dean Rd | Steel Barrier/Cones (A) |
| 08:00-09:00 | Linlithgow Rd/Dean Rd (Diversions out) | Rhino RB1/Road Closed |
| 08:00-09:00 | Dundas St/Linlithgow Rd | Cones/Road Closed |
| 08:00-09:00 | Cadzow Cres./Linlithgow Road | Steel Barrier/Road Closed |
| 08:00-09:00 | Braehead/School Brae/Cadzow Lane | Cones/Road Closed |
| 08:00-09:00 | Providence Brae/Stewart Avenue | Cones/Road Closed |
| 09:00-10:00 | Church Wynd/Panbrae Rd | Steel Barrier/Road Closed |
| 09:00-10:00 | Stewart Avenue/Church Wynd | Cones/Road Closed |
| 09:00-10:00 | Braehead Grove/Stewart Avenue | Cones/Road Closed |
| 09:00-10:00 | Church Wynd/Seaview Place R’about | Steel Barrier/Cones (B) |
| 09:00-10:00 | South Street junction with Seaview Place | Cones/Road Closed |
| 09:00-10:00 | Hope Street junction with North Street | Cones/Road Closed |
| 09:00-10:00 | Hamilton Lane junction with North Street | Cones/Road Closed |
| 09:00-10:00 | Market Street junction with North Street | Cones/Road Closed |
| 09:00-10:00 | East Pier St/North St | Cones/Road Closed |
| 09:00-10:00 | South St/North St | Cones/Road Closed |
| 09:00-10:00 | Commissionar St/Main St | Cones/Road Closed |
| 09:00-10:00 | The Bog/Main Street | Cones/Road Closed |
| 09:00-10:00 | Dock St/Links Rd | Cones/Road Closed |
| 09:00-10:00 | Grangepans/Boundary St | Cones/Road Closed |
| 09:00-10:00 | Starks Brae/Grangepans | Cones/Road Closed |
| 09:00-10:00 | Grangepans/Links Place | Cones/Road Closed |
| 09:00-10:00 | Grangepans/Park Lane | Cones/Road Closed |
| 09:00-10:00 | Grangepans/Cairns Ln | Cones/Road Closed |
| 09:00-10:00 | Grangepans/Dower Crescent | Cones/Road Closed |
| 09:00-10:00 | Grangepans/Rattray St | Cones/Road Closed |
| 09:00-10:00 | Grangepans/Dower Cres. | Cones/Road Closed |
| 10:00-11:00 | Bridgeness Rd/Cowdenhill | Rhino Rb1/Road Closed |
| 10:00-11:00 | Philpingstone Rd/Cowdenhill | Steel Barrier/Road Closed |
| 10:00-11:00 | Grange Terr./Grange Loan | Steel Barrier/Road Closed |
| 10:00-11:00 | Grahamsdyke Lane/Grange Loan | Cones/Road Closed |
| 10:00-11:00 | Grange Loan/Harbour Rd | Steel Barrier/Road Closed |
| 10:00-11:00 | Drumside Terrace/Harbour Road | Cones/Road Closed |

- Following the Closure of Side Roads along the Parade Route, Operatives will commence to close Main Arterial Roads (with corresponding Road Closure TM Signs) and Position themselves at Control/Pinch Points, once Road Closure established, this will occur on the timings of Table 2

Table 2

| Approx Time | Location | Equipment/Operatives |
| --- | --- | --- |
| 11:00 | Junction of Grahamsdyke Road and Harbour Road Shut | Steel Barrier and 2 Operatives with Radios (Police Presence Requested) |
| 11:15 | Junction of Deans Road (Linlithgow Road already shut between 08:00 and 09:00) | Rhino RB 1 Barrier and 2 Operatives with Radios (Police Presence if Available) |
| 11:30 | Junction Corbiehall Road at Seaview Place R’about | Steel Barrier and 2 Operatives with Radios (Police Presence Requested) |
| 11:45 | Junction of Bridgeness Rd and Cowdenhill | Rhino RB 1 Barrier (Unmanned) |
| 11:50 | Grange Terr/Grange Loan Access | Steel Barrier and 1 Operative |
| 12:00 | Kinglass and Gauze Road (placed out between 08:00 and 09:00) | 2 Operatives drop off to look after this area |
| 12:00-13:00 | All areas Patrolled and vans position themselves are start and end of Parade | Two Pickup vans and 2 Operatives in each |

- Operatives will be constant Radio Contact with Mobile Phone back up, if interference occurs. This will keep Operatives up to date with Emergency Service movements, the Parade movements and progression and preparation for completion of the Parade

Site Access and Exits

- Access to Roads will only be granted to Emergency Services and directed in the areas/times stated in drawing 17-Bo’ness-ch-Fr-fest-001, which will be presented to the relevant services by the Fair Committee.

- Access for Buses and Bands at Grange Terrace and Loans will be monitored by Operative based in this area. This Operative will also keep a look out for Bridgeness Road/Cowdenhill Rd Junction

Emergency Services

- Access to Roads from the Emergency services will be given in accordance to the times stated in drawing 17-Bo’ness-ch-Fr-fest-001. This drawing will avoid undue risk to services entering the Parade area and access can be gained from side roads. Emergency Services must take due care when accessing the closed off areas, as Pedestrians may be in the vicinity and due care is to be taken when passing through the closed off area of the town.

Traffic Management Maintenance

This should include as a minimum, prior to Parade and During:

- Two Patrol Vans will Patrol route prior to commencement of Parade and follow the parade In Front and Behind.

- Radio Contact (mobile phone backup) maintained with All Operatives and Lead Personnel of Fair Committee

Traffic Management Removal (Parade Completed)

Approximately (depending on Parade Delays) between 14:00 and 14:30, Operatives will start to open up/remove Traffic Management from the Main Arterial Pinch Points and side streets, once confirmed that Parade has left the Main Routes. The General sequence will be as follows :

- Patrol Vehicles will start to Open up the roads/side streets from Seaview Place, North St to Links Road

- The Opening of Roads and Side streets will continue in a Clockwise sequence until Junction with Dean Road and Linlithgow Road.

- Grahamsdyke Road/Harbour Rd Junction and Junction with Dean Rd/Linlithgow Rd will be opened at the same time to allow continuous flow.

Traffic Management Equipment Removal (after event)

The majority of Traffic Management equipment will be set aside after the period in a safe and secure manner, with Operatives coming in at the evening to remove Cones, Steel Barriers/Rhino RB1 from the streets, once the crowds from the day have dispersed to a sufficient level to carry out these works.

The collection works will take place on Friday Night/Saturday morning after the event.

Revision Status

| Revision | Date | Amendment | Content Owner | Authorised By |
| --- | --- | --- | --- | --- |

Appendices (see maps)

17-Bo’ness-ch-Fr-fest-001-Final – Emergency Route Map

17-Bo’ness-ch-Fr-fest-002-Final  - Traffic Management Drawing

Risk Assessment

| Activity Description: | Bo’ness Children’s Fair Festival Traffic Management |
| --- | --- |
| ID | Hazard | Adverse Effects | Persons Affected | Control Measures | A | S | L | R with controls in place | T |
| 1 | Planning Parade Route Works | Fatal or Serious Injuries due to Incursions | Public and workforce | Assess the location of the proposed works to ensure it is safe and practicable for implementation and removal, taking into account - Road Users, Emergency Services, Workforce and General Public | Y | C | HU | 4 | Y |
| 2 | Weather Conditions | Fatal or Serious Injuries due to RTC’s | Public and workforce | Assess conditions prior to works starting and agree progression with Fair Committee any changes or re-routes | Y | C | HU | 4 | Y |
| 3 | Advance signage | Fatal or Serious Injuries due to RTC’s | Public and workforce | Advance signage should be as per this Method Statement/Drawing and Red Book Legislation | Y | C | HU | 4 | Y |
| 4 | Sharp Edges of Sign Faces or Frames | Cuts and Abrasions | Workforce | Wear good abrasion gloves | Y | I | HU | 3 | Y |
| 5 | Poor Standard of Pedestrian/Road Barrier | Various Injuries from Moving vehicles, slips, trips and falls | Public and workforce | Pedestrian Barrier to have sure footing and linked together appropriately. Rhino RB1 Barrier to be linked together to form a robust system Cones to be Placed together in a row. Areas of frequent incursions, should be roped | Y | I | HU | 3 | Y |
| 6 | Parking vehicles whilst setting up T.M. | Fatal or Serious Injuries | Public and workforce | On Public (Council) roads where possible any convenient layby, field, gateway, or side road may be used. If stopping on the carriageway is the only location available, park as close to the edge as possible. This is especially relevant when using mobile closure techniques or short duration stops on roads. | Y | I | HU | 4 | Y |
| 7 | Site Access and Exits | Fatal or Serious Injuries due to Incursions | Public and workforce | Manned Pinch Point Areas along the routes with Rhino RB1 barrier. Internally out with Pinch Points Steel Barrier and Cones | Y | C | HU | 4 | Y |
| 8 | Third Parties Affected by Your Parade | Fatal or Serious Injuries due to RTC’s | Public and workforce | Assess the location of the proposed works to ensure appropriate consultation and provision has been made | Y | C | HU | 4 | Y |
| 9 | Vehicles entering the Parade Area | Death due to Collision with vehicle | Workforce and Public | A solid barrier and a Operatives located at Pinch points along route. Radio/Mobile Phone communication for all teams | Y | I | L | 4 | Y |
| 10 | Vehicles entering the site through coning | Death due to Collision with vehicle | Workforce and Public | Solid coning before the works area with Inspection prior to Parade may be considered. Vehicle Aligned in front of Parade and Behind Parade. Radio Contact at all times | Y | I | L | 4 | Y |
| 11 | Site Specific Hazards at time of Implementation | All Parties Concerned | Workforce and Public | Risk Assess the site, prior to implementation. Patrols Carried out prior to and during parade Manned Accesses at Pinch Points | Y | C | HU | 4 | Y |
| 12 | Emergency Services entering the closed off works area | Death due to Collision with vehicle | Workforce and Public | Emergency Services given prior notice of Timings and caution when entering site, submitted to the relevant services by the Fair Committee. Emergency Services to adhere to best practice when in Parade area | Y | T | HU | 1 | Y |
| 13 | Pre Setting, Implementing and Removing Traffic Management | Injury, Slips, Trips and Falls | Workforce and Public | Ensure when pre-setting all Traffic Management and Barrier, that it is done so to not hinder or block access to Pedestrians either via walking or wheeled motion. Equipment should be within location with hindering access prior to parade, but as such to aid locating during works. Implementation/Removal as per Method statement. Ensure Parade traffic off route prior to Removal. Contact maintained with Parade contacts for any changes | Y | I | HU | 3 | Y |
|  | Manual Handling | Injury | Workforce | Pre-setting of Equipment prior to event will reduce the excessive need for manual handling at the event. Ensure Operatives use Pristine Condition Training techniques such as Dip n Drive, Inside Base and Tandem Lifts/Mechanical movements. Movements of Barrier to be conducted in Groups of Two to share the burden. Pre-setting should involve Hiab and Beavertail Loaders. | Y | S | U | 3 | Y |
|  | Unaware Public and Residents | Traffic Incursions and Injury | Public and Works | Advance Signage to be erected by WC 12th June, informing Public and residents of the Road restrictions with Date and times. Fair Committee to inform all Local Residents of the events and sequence of Parade movements via various media outlets (Facebook, Letter drops, Twitter and Website) | Y | C | HU | 3 | Y |

Key: A=ALARP insert Y or N, S=Severity (T / M / I / S / C), L=Likelihood (HU / U / L / VL / C), R=Risk Classification (1 / 2 / 3 / 4 / 5), T=Tolerable? Insert Y or N